07-05-19 Test Devlog
1. Power Control system does not print the correct interval time to the serial monitor.
  1. Bug in the serial monitor system prevented the number from being printed properly. Works fine.
2. Remove multiple eeprom read/write locations because it is too complex
3. MAINPROGT2 for Julian to carry out., waiting for the pin spreadsheet.
4. Satellite and ground station go out of sync for around 5 seconds after the RTTY transmit.
5. It is possible to receive a pong command and transmit a ping command in the same sketch but it has a low probability of being received.

1. The demonstration electronics does not receive the power information packet.
2. The demonstration ground station does not receive both the FOSSASAT-15 packet and the FOSSASAT-19 packet when both are being sent.
  1. Put a delay between the power information transmission and the other transmission cycles.
    1. No effect
  2. Implemented a 1 second delay between transmission of power information and communications system
3. There might be an internal delay with the interrupt service routine.

1. Leaving the satellite ground station running for about 10 minutes to ensure the screen updates correctly.
2. As long as the transmissions to the satellite are received correctly, the response is not critical since the system information packet should describe its status.
  1. Alternatively, we can loop and transmit a response packet X amount of times.

Talking to Julian about the low probability of receiving an individual packet.